## Slide 1
Ventura County Traffic Model (VCTM)
VCTC Update
April 6, 2018

## Slide 2: VCTM– A Long History!
First VCTM developed in 1992 with updates and conversions throughout the years with the last update completed in 2009.
Land Use Based (Building Square Footage and LU Acres)
Autos only (No Transit or Goods Movement/HDT Component)
New VCTM developed to Meet Key Application Needs
  Environmental Analyses
  County General Plan Update
  SB 743
  Impact Fee/Fair Share Needs
  Next Generation of Local Models

## Slide 3: VCTM Consistency
VCTM must be consistent with SCAG 2016 Regional Transportation Plan (RTP)/Sustainable Communities Strategies (SCS) Regional Travel Demand Model
  Subarea Model Development Tool
SCAG Zone Structure
  11,000+ zones – Used for trip distribution and mode choice
  Full Model run time upwards of 7-10 days
VCTM
  663 Ventura County zones
  Base Year 2012 – Forecast Year 2040
  1,021 total zones
  Full Model run time 13-15 hours.

## Slide 4: Traditional Four-Step Model Process Tries to Replicate Human Travel Behavior
Trip Generation
  Do I make a trip?
Trip Distribution
  Where do I go?
Mode Choice
  What are my means of travel?
Assignment
  What route do I choose?

## Slide 5: Model Calibration & Validation (Comparing Model Outputs to Real World Counts)
What needs Calibration?
  Trip Generation Rates and External Trips
  Trip Distribution Parameters
  Mode Choice Coefficients
Freeway and Arterial Street Validation Criteria
  Count/Volume Comparison (FHWA & Caltrans)
    Freeways +/- 7%
    Major Arterials +/- 10%
    Minor Arterials +/- 15%
  Percent Root Mean Squared Error (%RMSE )
    Caltrans = 40 and FHWA = 30
  Coefficient of Determination (R2) (FHWA & Caltrans)
    0.88
  Caltrans Standard Deviation
    >0.75
Caltrans Criteria from the Caltrans Travel Forecasting Guidelines, November 1992
FHWA Criteria from the TMIP Model Validation and Reasonableness Checking Manual

## Slide 6: Model Validation Results

## Slide 7: Model Outputs
Performance Measures
All outputs developed for the following:
  Ventura County, General Plan Districts, TIMF Districts, Cities
  By Time of Day (AM peak period, Mid-day, PM peak period, Evening, Night)
Performance Measures
Assignment Loading (Volumes and Speeds)
Internal/External Origins & Destinations
V/C Ratios on Facilities
Heavy Duty Vehicle Volumes
Transit Ridership by Mode
Active Transportation Modes
Model Application
Functional Class Plots
  With number of lanes
  With Speeds
Volume to Capacity Plots
Air Quality Speed Bin Outputs
Automated Outputs
  Vehicle Miles of travel
  Vehicle Hours of travel
  Vehicle hours of delay

## Slide 8: AM Peak Period (6-9 AM)
2012 Validation
  VMT = 3,249,750
  VHT = 79,550
  VHD = 13,200
  Average Speed = 40.9 MPH
2040 Baseline
  VMT = 3,714,000
  VHT = 104,150
  VHD = 26,850
  Average Speed = 35.7 MPH

## Slide 9: PM Peak Period (3-7 PM)
2012 Validation
  VMT = 5,090,500
  VHT = 129,300
  VHD = 24,100
  Average Speed = 39.4 MPH
2040 Baseline
  VMT = 5,717,150
  VHT = 163,200
  VHD = 42,900
  Average Speed = 35.0 MPH

## Slide 10: Average Daily Traffic
2012 Validation
  VMT = 16,588,600
  VHT = 386,800
  VHD = 45,700
  Average Speed = 42.9 MPH
2040 Baseline
  VMT = 18,850,900
  VHT = 475,700
  VHD = 83,000
  Average Speed = 39.6 MPH

## Slide 11: Average Daily Traffic (ADT) and Vehicle Hours of Delay (VHD) U.S. 101
Chart: 
| AM Peak Period | PM Peak Period | Average Daily
VHD 2012 | 5787.512 | 10319.2258 | 19150.9335
VHD 2040 | 11337.1035 | 16901.353 | 33026.9261
150,622
63,945
80,497
162,642
146,252
157,805
191,821
203,849
166,597
172,924
(2012)
(2040)
(2012)
(2012)
(2012)
(2012)
(2040)
(2040)
(2040)
(2040)

## Slide 12: Vehicle Miles Traveled (VMT) by Speed
Increase in low speed VMT
Decrease in high speed VMT
Overall increase in VMT of 14%
Chart: 
| Average Daily VMT
2040 | 18850871.0019
2012 | 16588580.3833
blank | 0
2040

## Slide 13: Mode Choice Outputs
Similar Mode Splits between 2012 and 2040
Transit Trips 1 – 1.114%
Non-motorized Trips 4.79 – 5.0%
Increase in total number of trips
  3,220,374 (2012) – 3,780,041(2040)

## Slide 14: Next Steps
Coordination with General Plan
US-101 HOV Lane
Local Applications and Updates

## Slide 15
Ventura County Traffic Model (VCTM)
VCTC Update
April 6, 2018